## Slide 1
Introduction to Secure File Transfer Systems
SocketVault: Secure File Transfer System Using TCP | Computer Networks Lab | A467502 | B21
1
File transfer is one of the most fundamental operations in computer networking.
Traditionally handled by FTP, SFTP and SCP, all built on top of TCP.
Existing tools are opaque black boxes that hide the mechanics of socket programming.
SocketVault is built from the ground up in C using raw POSIX TCP sockets, showing every layer of the transfer explicitly.
It bridges theory and practice: a raw TCP transfer engine plus a modern web dashboard for real-time file management.
Relevance
Understanding how TCP sockets work is fundamental to understanding the Internet itself.

## Slide 2
Existing File Transfer Systems
SocketVault | Computer Networks Lab | A467502 | B21
2
System | Key characteristics
FTP | Oldest standard. Two TCP connections (control + data). No native encryption.
SFTP | Encrypted FTP over SSH. Secure but complex key management.
SCP | Simple, fast, SSH-based. Command-line only, no UI.
HTTP/HTTPS upload | Used by web apps. Hides TCP entirely behind high-level libraries.
Dropbox / Drive / OneDrive | Consumer tools on massive infrastructure. No visibility into the networking layer.
All of these are either too high-level (hiding the socket layer) or too complex to set up for a lab environment.

## Slide 3
Limitations of Existing Approaches
SocketVault | Computer Networks Lab | A467502 | B21
3
No transparency
FTP and SFTP don't expose bind(), listen(), accept() and send() in action.
External dependencies
Most tools need OpenSSL, third-party libraries or system daemons.
Not educational
Production-grade and optimized; unsuitable for learning TCP at byte level.
No protocol control
Can't define your own message framing, chunking or handshake.
No Web UI
CLI tools lack a visual interface to demonstrate results in a viva.
Platform lock-in
Tied to specific OS setups or require root privileges.

## Slide 4
Proposed Solution: SocketVault
SocketVault | Computer Networks Lab | A467502 | B21
4
A custom-built, dual-protocol server written entirely in C.
Raw TCP file transfer engine on Port 9000 for authentic socket-level communication.
Lightweight HTTP/1.1 API server on Port 8000, built from scratch with C sockets, powering a React Web Dashboard.
Zero external libraries: only <sys/socket.h>, <arpa/inet.h>, <pthread.h>, <dirent.h>.
Files move in 64 KB binary chunks directly between sockets, showing stream-based TCP behavior.
Makes TCP socket programming observable, interactive and demonstrable.
Port 9000
Raw TCP
File transfer engine
Port 8000
HTTP/1.1 API
Feeds the React dashboard

## Slide 5
Key Features of SocketVault
SocketVault | Computer Networks Lab | A467502 | B21
5
Raw TCP Sockets in C
socket(), bind(), listen(), accept(), send(), recv().
Multi-threaded Server
pthread_create() handles simultaneous clients without blocking.
Chunked File Streaming
Any file type in 64 KB blocks for memory efficiency.
Built-in HTTP API
Hand-crafted HTTP/1.1 parser: GET, POST, DELETE, OPTIONS (CORS).
Modern Web Dashboard
React + Vite, glassmorphism UI for upload, download and management.
Path Traversal Protection
Filenames sanitized with strrchr() to block directory traversal.
No External Dependencies
One gcc command. No CMake, no package managers.

## Slide 6
System Architecture Overview
SocketVault | Computer Networks Lab | A467502 | B21
6
C TCP Client
client.c
React Dashboard
App.jsx
C Server
server.c + http_api.c
storage/uploads/
shared directory
TCP :9000
HTTP :8000
One entry point boots two listeners at startup.
server.c: pthread_create() spins a thread per TCP client.
http_api.c: dedicated background pthread parsing raw HTTP.
Both read/write the same ./storage/uploads/ directory.
React talks only HTTP (8000); TCP (9000) is reached via the C client.

## Slide 7
Detailed Component Breakdown
SocketVault | Computer Networks Lab | A467502 | B21
7
Component | File | Language | Role
TCP File Server | server.c | C | Accepts raw TCP connections, spawns threads, saves uploads to disk
HTTP API Server | http_api.c | C | Parses HTTP, lists files, handles browser uploads/downloads, sends CORS headers
C TCP Client | client.c | C | Connects to port 9000, streams files with send()/recv()
Web Dashboard | App.jsx | React / JS | Upload button, file list and download buttons via HTTP calls
Shared Storage | storage/uploads/ | File system | Single directory read by both the TCP server and the HTTP API

## Slide 8
File Upload Flow (TCP Path and HTTP Path)
SocketVault | Computer Networks Lab | A467502 | B21
8
TCP upload (1/2)
Client starts: gcc -o client client.c, then ./client 127.0.0.1 U myfile.pdf
socket() creates the TCP socket
connect() to IP:9000; 3-way handshake completes
Send 1-byte command (U) + 255-byte filename buffer
fread() loop reads 64 KB chunk, send() pushes it over the socket
TCP upload (2/2)
Server accept() unblocks; pthread_create() spawns handler thread
Thread recv() loop; fwrite() each chunk to ./storage/uploads/
EOF: client calls close() on the socket
recv() returns 0; server closes file, thread exits
File is in storage; Dashboard shows it on next Refresh
HTTP upload
User clicks Upload File; browser reads file as binary
React sends POST /api/upload with X-Filename header + binary body
Server recv() reads headers; extracts Content-Length and X-Filename
Server opens path; streams body bytes into file with fwrite()
Server sends 200 OK JSON; React refreshes file list

## Slide 9
Results & Demonstration
SocketVault | Computer Networks Lab | A467502 | B21
9
Transferred files of varying sizes (text 37 Bytes, DOCX 25.46 KB) via raw C TCP sockets.
Server handles multiple simultaneous clients using POSIX threads.
Dashboard shows all uploaded files with real sizes in real time.
Download works via the C client (D command) and the browser's Download button.
Backend compiles in one command: gcc -o server server.c http_api.c -lpthread
SocketVault Dashboard (illustrative mockup)
notes.txt
37 B
Verified TCP
Download
Delete
report.docx
25.46 KB
Verified TCP
Download
Delete
Replace with your real dashboard screenshot before presenting.
Note: ran locally on macOS; deployable to Render (C backend) and Vercel (React frontend) on free tiers.

## Slide 10
Conclusion
SocketVault | Computer Networks Lab | A467502 | B21
10
SocketVault demonstrates the full lifecycle of a TCP file transfer, from the kernel socket layer to the web dashboard, with no external networking library.
Transport (TCP) and Application (HTTP) layers run side by side in one C executable using POSIX threads.
Students gain hands-on exposure to raw sockets, threads and HTTP header parsing.
Future scope: SHA-256 checksums (OpenSSL) for integrity, TLS encryption, user authentication.
API surface
socket() bind() listen() accept() connect() send() recv() pthread_create()
Open source: github.com/shankumar7/SockerVault
Thank you!